## Slide 1: FULL-SCALE THERMAL TREATMENT OF AGENT ORANGE DIOXINS AT DANANG AIRPORT, VIETNAM
Kent Sorenson CDM Smith
Jeff Bamer CDM Smith
Alexis Lopez CDM Smith
Pete Chenevey CDM Smith
Randa Chichakli CDM Smith
Ralph Baker TerraTherm*
Gorm Heron TerraTherm
Tom Boivin Hatfield Consultants*
Maura Patterson USAID*
*formerly

## Slide 2: Acknowledgements
This work is funded and overseen by USAID. Special thanks to:
  Michael Greene
  Joakim Parker
  Chris Abrams
  Kyung Choe
  Jim Brown
  Maura Patterson
  Andrew Sayers-Fay
  Phuc Nguyen

## Slide 3
Operation Ranch Hand – herbicides for defoliation
Agent Orange contained dioxin as 2,3,7,8-TCDD
Over 100,000 barrels used at Danang
USAID lead agency for cleanup at Danang
Danang Airbase - 1972
Agent Orange Use at Danang

## Slide 4
Discrete soil and sediment samples collected through January 2010
Danang Airport
Notes: Talk about different areas, hot spots, hydrology

## Slide 5
Environmental Assessment (EA) Site Characterization Information
  ~89 discrete soil/sediment samples from previous studies
  34 discrete soil samples collected during EA (11 exceeding standard)
  28 discrete sediment samples collected during EA (11 exceeding standard)
Environmental Assessment (EA) Sampling

## Slide 6: Remedy
Design excavation areas
~20 Ha total area
15 cm to > 3 m depth
Eastern Hot Spot: 1.9 Ha
Sen Lake and Wetland: 11 Ha
Drainage Ditch: 3.4 Ha
Former Storage Area: 1.7 Ha
Mixing and Loading Area: 1.4 Ha

## Slide 7: Remedy
Two-phased implementation
“Upland” in Phase 1
Primarily sediments in Phase 2
Phase II
Phase I
IPTD Pile

## Slide 8
EA evaluated four alternatives:
  No Action
  Passive Landfill
  Active Landfill (Bioremediation)
  In-Pile Thermal Desorption® (IPTD®) - patented by Royal Dutch Shell and further developed by the exclusive licensee, TerraTherm, Inc.
Environmental Assessment (EA) Remedy Selection

## Slide 9
EA Remedy Selection (cont.)
°C
= 335C
100
200
300
400
Heater
Heater
t2
t3
t1,2,3 = temperature progression
t1
IPTD® selected based on:
  Effectiveness: only alternative proven to destroy dioxin to Vietnam dioxin standards for soil (1,000 ppt) and sediment (150 ppt)
  Implementability: all alternatives implementable at Danang Airport
  Environmental Impact: IPTD® had lowest potential environmental impact
  Cost: IPTD® cost estimate in same range as other alternatives when long term landfill O&M was considered
Destruction depends on both temperature and time

## Slide 10
Applicability to Dioxins
IPTD®

## Slide 11
Pre-treatment 2,3,7,8-TCDD concentrations
  Soil: 130,000 ppt to 157,000 ppt (VN standard = 1,000 ppt)
  Sediment: 5,970 ppt to 7,480 ppt (VN standard = 150 ppt)
Post-treatment 2,3,7,8-TCDD concentrations
  MLA Soil below soil cleanup goal (1,000 ppt) after 10 days
  Sen Lake Sediment below sediment cleanup goal (150 ppt) after 7 days
Danang Airport Treatability Testing

## Slide 12
Treatability Testing Results

## Slide 13
Pile Structure
Grade Level
Insulated Sidewall Panel
Steel Sheeting
Drain Piped to Sump
Drainage Layer
Insulated Floor
Insulated Surface Cover
Air Inlet Well
Heater-Only Well
Horizontal Vapor Extraction Well
Excavated Soil
Conceptual design - fully contained and insulated structure
Note: design evolved after the EA from an above ground stockpile of contaminated soil/sediment surrounded by clean soil berms to an insulated concrete structure
IPTD® Pile Design

## Slide 14
Dimensions: 105 m X 70 m X 6 m
Capacity: 45,000 m3
Heater well spacing: 2.7 m (8.9 ft)
# heater wells: 1,254
# temperature monitoring wells: 56
# pressure monitoring wells: 8
# air inlet wells: 202
IPTD® Pile Design

## Slide 16
Phase 1 Results – Calculated average pile temperature
Notes: Shows the calculated average pile structure temperature.
Average pile temperature is representative of all the temperature sensors installed in the soil interval from 30-600 cm.

## Slide 17
Phase 1 Results – Average centroid temperature by treatment zone depth interval (10 mo. heating)
Notes: Shows the average target treatment zone (TTZ) centroid temperature by depth layers. Even though the average target temperature was reached on January 14, 2015, several layers, especially the upper part of the pile, were lagging in temperature, while the mid-depths of the pile were substantially warmer, bringing up the average pile temperature. An average temperature of 335°C (635°F) was not reached in the top 30 cm pile layer until March 25, 2015. At that point all layers from 200 to 500 cm in the pile had reached an average temperature at or above 490°C (914°F).
On March 16, 2015, confirmatory soil sampling was initiated. Based on the results, the heaters were deenergized on April 9, 2015. At that point the highest average temperature was recorded for the 300 cm layer at 577°C (1,070°F).

## Slide 18
Phase 1 Results – Average soil temperature vs. depth at pile interior
Notes: Shows the vertical profile by depth of the average temperature of all interior thermocouple locations.
The average temperature at all depths decreased slightly in the latter part of the month of April. As of April 30th, the average interior temperatures throughout the entire depth of the pile ranged between approximately 360C and 550C.

## Slide 19
Must confirm average concentration < 150 ppt
Pile divided into six, 1-m decision units vertically (DU layers)
Modified “pot-holing” used to collect samples
Triplicate collected for one layer
-1 m
-0 m
-2 m
-3 m
-4 m
DU-1
DU-2
DU-3
DU-4
Core Increments
30 Borings
Application of Incremental Sampling Methodology to Treatment Confirmation

## Slide 20
Sample ID | Location | Date Sampled | Action Level (pg TEQ/g) | Dioxin Concentration (pg TEQ/g)
1R-SL-P1-IPTD-0001 | Phase I IPTD samples collected at A locations, 0-1m | 3/23/2015 | 150 | 51.5
1R-SL-P1-IPTD-0002 | Phase I IPTD samples collected at B locations, 1-2m | 4/25/2015 | 150 | 0.332
1R-SL-P1-IPTD-0003 | Phase I IPTD samples collected at B locations, 2-3m | 4/25/2015 | 150 | 0.237, 2.34, 0.27 95% UCL = 2.6
1R-SL-P1-IPTD-0004 | Phase I IPTD samples collected at B locations, 3-4m | 4/25/2015 | 150 | 0.304
1R-SL-P1-IPTD-0005 | Phase I IPTD samples collected at B locations, 4-5m | 4/25/2015 | 150 | 0.0918
1R-SL-P1-IPTD-0006 | Phase I IPTD samples collected at B locations, 5-6m | 4/25/2015 | 150 | 0.981 (lab dup 0.819)
Phase 1 Final Sample Results (May 2015)
95% UCL = 2.6 pg/g
Depth (m)

## Slide 21
Phase 1 pile was quenched May-July 2015
Phase 1 treated soil/ sediment was removed September-October 2015
Temporary storage area for Phase 1 treated material
Removal of Phase 1 treated soil/sediment
Cooling and Removing Treated Material

## Slide 22: Phase 2 Modifications
Design
  Heaters
  Cover
  Liquid Vapor Treatment Plant (LVTP) Modifications
Mass Balance
  Collect initial ISM samples in pile
  Increased sampling of LVTP processes
Ready for Phase 2!

## Slide 23: Modified Heater Design
Bottom 2m boost

## Slide 24: Cover Redesign
210 kg/cm2
210 kg/cm2

## Slide 25
Phase 2 Pre-treatment Concentrations by ISM
+/- 275 pg/g
Depth (m)

## Slide 26
Phase 2 Results – Average centroid temperature by treatment zone depth interval (6 mo. heating)
Notes: Shows the average target treatment zone (TTZ) centroid temperature by depth layers. Even though the average target temperature was reached on January 14, 2015, several layers, especially the upper part of the pile, were lagging in temperature, while the mid-depths of the pile were substantially warmer, bringing up the average pile temperature. An average temperature of 335°C (635°F) was not reached in the top 30 cm pile layer until March 25, 2015. At that point all layers from 200 to 500 cm in the pile had reached an average temperature at or above 490°C (914°F).
On March 16, 2015, confirmatory soil sampling was initiated. Based on the results, the heaters were deenergized on April 9, 2015. At that point the highest average temperature was recorded for the 300 cm layer at 577°C (1,070°F).

## Slide 27
Phase 2 Results
Notes: .

## Slide 28
Phase 2 Final Sample Results (June 2017)
95% UCL = 0.24 pg/g
Depth (m)
99.99% Removal for all Decision Units

## Slide 29
Pre-design investigation through complete site cleanup achieved in less than 9 years
IPTD met stringent treatment standard with >99.99% removal
ISM for confirmation sampling minimized variability
Danang Airport will be ready for transfer in 2018
Conclusions

## Slide 30
Questions?